Troubleshooting Actions

Triggered by Maintenance Diagnostics

Summary

The assumption is that schedule maintenance was proceeding when a maintenance diagnostic uncovered a failed part. The maintenance action follows the unsuccessful outcome, that is, a troubleshooting action is initiated.

All “maintenance triggered” troubleshooting actions also have an “operational failure” triggered troubleshooting action for the same equipment component. The maintenance triggered troubleshooting actions generally have a reduced time-to-resolve given that the part problem was discovered prior to its operational failure.

The following section describes how the maintenance and troubleshooting XML documents are matched according the equipment EIC and Name. Maintenance “unsuccessful outcome” equipment information will be matched against the troubleshooting “trigger” equipment information to determine the sequencing. It is assumed that maintenance scheduling occurs before any maintenance action and that troubleshooting reporting follows any troubleshooting action. Thus the final sequence of XMLs looks like this:

maintenance     +         maintenance                +     troubleshooting    +   troubleshooting

scheduling            action (unsuccessful)                    action                       reporting

Example of sequencing the maintenance and troubleshooting XMLs

The TSSID identifies the “job-based” crew action identifier in the XML document collection. For the TSSID troubleshooting action listed in column 3 of the table, the troubleshooting XML document is named as follows

<EquipmentCategory> TSSID<TSSID#>  maint.xml

For example, if TSSID=1, the troubleshooting XML document is

Power Gen TSSID1 maint.xml

and  the troubleshooting action was triggered by the maintenance XML document

Power Gen MRC GTG Motor.xml

Both XML documents (maintenance and troubleshooting) refer to an equipment component identified as

3510000 GTG AUX PUMP MOTOR, AC

That is,

<equipmentEIC>3510000</ equipmentEIC>

<equipmentName>GTG AUX PUMP MOTOR, AC</equipmentName>

is the trigger match for “unsuccessful” outcome of the maintenance action leading to troubleshooting.

The match up table for maintenance to troubleshooting

Below is the table listing the maintenance trigger XML match-ups with the troubleshooting XML for the given TSSID.

| Equipment Category | Equipment EIC, Equipment Nomenclature Component Specification for Trigger | TSS ID | Maintenance Trigger XML document |
| --- | --- | --- | --- |
| Power Dist | 4103000 ACSFC INVERTER, BLOWER MOTOR | 36 | Power Dist MRC Blower Motor |
| Power Gen | 3510000 GTG AUX PUMP MOTOR, AC | 1 | Power Gen MRC GTG Pump Motor |
| Power Gen | 3510000 GTG COUPLING, FLEXIB | 2 | Power Gen MRC GTG Flexib |
| Power Gen | 3510000 GTG VALVE, CONTROL TEMP | 3 | Power Gen MRC GTG Temp Control |
| Power Gen | 3510000 NOZZEL, FUEL ASSEMBLY THERMOCOUPLE | 4 | Power Gen MRC Fuel Nozzle Therm |
| Power Gen | 3510000 LOCAL CONTROL PANEL POWER SUPPLY | 5 | Power Gen MRC Locop PS |
| Power Gen | 3510000 LOCAL CONTROL PANEL FUEL TEMP CARD | 6 | Power Gen MRC Locop Fuel Temp |
| Power Gen | 3510000 GTG STARTER ASSEMBLY | 7 | Power Gen MRC GTG Starter Pad |
| Power Gen | 3510000 GTG NO-B POWER SUPPLY | 8 | Power Gen MRC GTG NoB PS |
| Power Gen | 3510000 GENERATOR SET MORMON CLAMP | 9 | Power Gen MRC GenSet Mormon |
| Power Gen | 3510000 PUMP, MAIN PRESS | 10 | Power Gen MRC Pump Main Press |
| Power Gen | 3510000 LOCAL CONTROL PANEL WATER WASH SWITCH | 11 | Power Gen MRC Locop Water Wash |
| Power Gen | 3510000 LOCAL CONTROL PANEL RPM METER | 12 | Power Gen MRC Locop RPM Meter |
| Power Gen | 3511000 GENERATOR SET SK GAGE LINE | 13 | Power Gen MRC GenSet Gage Line |
| Power Gen | 3511000 GOVERNOR, ELECTRIC EHGA VALVE | 15 | Power Gen MRC EHGA Valve |
| Power Gen | 3511000 ENGINE ASSEMBLY GTG BLEED AIR SPLIT LINE | 17 | Power Gen MRC Engine Assy BAS Line |
| Power Gen | 3511000 ENGINE ASSEMBLY GTG THERMOCOUPLE | 18 | Power Gen MRC Engine Assy Therm |
| SLQ32 | N87K000 AN/SLQ32 HVSU Relay | 250 | SLQ-32 MRC B1 EXA3 |
| SLQ32 | N87K000 AN/SLQ32 ANTENNA BLOWER MOTOR | 251 | SLQ-32 MRC 41 ETF4 N |